Chapter 15 Electric Charges and Electric Fields

15.1	Electric Charge and the Electrical Electric Fields 578

15.2	Transfer of Electric Charge 581

15.3	Electric Forces - Coulomb’s Law 585

1.	      =   	1 elem chg = 1.602 x 10-19 C

1 C = 6.24 x 1018 elem chg

2.	sp	588		1	2

3.	pp	589		1	2	3

4.	Fgravitational electron on protron	me = 9.1 x 10-31kg	mp = 1.7 x 10-27 kg

5.	Felectrical electron on protron	qe = 1 elem chg		qp = 1 elem chg    d = 5.3 x 10-11 m

6.

7.	sp 	590		1	force on charge in middle	2	force with 4 charges

8.	pp	592		1	2	3

9.	ecp	620		13    14    15    16    17    18    19

15.4	Electric Fields 593

1.	Every charged object creates an electric field of force in the space around it.

2.	Electric field represented by drawing a series of force vectors

3.	“electric field intensity”     where Q is charge on sphere

4.	direction is direction of force on a ‘+’ charge placed at the position

5.	 of parallel plates is ’q’ where ‘q’ is the on the plate   [a uniform electric field]

6.	sp 	596		1	2	3

7.	pp	597		1	2	3	4	5	6	7

8.	ecp	621		20    21    22    23

15.5	Electric Potential  599

1.

2.	‘V’ electric potential =

represents the amount of work to move a unit positive test charge from infinity to rest at any specific point in the field of Q

3.	more common to think of work to move a test charge from one point to another in the field

4.	potential difference or voltage difference

5.	  =    =

6.	     thus

7.	sp	602		1	2	3	4

8.	pp	603		1	2	3	4

9.	ecp	622		24    25    26    27    28

15.6	Electrical Fields Inside and Surrounding a Conductor  603

1.	Any charge placed on an insulated conductor resides entirely on the outer surface or

the electrical field inside a conductor is zero

2.	Example TV wire in center with cylinder of oven fine wires or aluminum foil on the outside

15.7	The Millikan Experiment-Determination of the Elementary Charge 605

1.	e = 1.602 x 10-19 C

2.	sp	608		1	2

3.	pp	609		1	2	3	4	5	6

15.8	The Motion of Charged Particles in Electric Fields  610

1.

2.

3.	sp	611

4.	sp	612

5.	pp	613		1	2	3	4	5

6.	ecp 623		30   31   32   33   34   35   36   37   38   39   40