VOYAGER MISSION OPERATIONS STATUS REPORT #1085, AUGUST 14 THROUGH AUGUST 20, 1999

COMMAND TRANSMISSION & VERIFICATION OPERATIONS

Voyager 1 command operations consisted of a command loss timer reset on 08/17 [DOY 229/1830z]. The spacecraft received the command.

Voyager 2 command operations consisted of the uplink of seven bracketed command loss timer resets, sent on five-minute centers using 0.5 Hz steps, on 08/18 [DOY 230/1157z] at DSS-43. The spacecraft received elements two through six of the seven sent.

SEQUENCE GENERATION OPERATIONS

Submitted draft Sequence Requests for CCSL A033 to the SIE

.

DATA RETURN OPERATIONS

Voyager 1 Data Processing and Operations:

There were 103.9 hours of DSN scheduled support for Voyager 1 of which 85.1 hours were large aperture coverage. There were no real-time or schedule support changes or significant outages during the period.

Science instrument performance was nominal for all activities during this period. One frame of GS-4 data was recorded this week with the PLS modulator switched off. The EDR backlog is 9 days.

Voyager 2 Data Processing and Operations:

There were 86.0 hours of DSN scheduled support for Voyager 2 of which 44.4 hours were large aperture coverage. There were no real-time or schedule support changes made during the period.

There was one significant outage on 8/20 [DOY 232] when 4.0 hours of data were degraded due to unknown causes at DSS-42 [DR A03934].

Science instrument performance was nominal for all activities during this period. One frame of GS-4 data was recorded this week. The EDR backlog is 9 days.

FLIGHT SYSTEM PERFORMANCE

Voyager 1 performance was nominal during this report period. Major activities included DTR Maintenance and a PMPCAL on 8/17 (DOY 229/230).

Voyager 2 performance was nominal during this report period.

PROPELLANT/POWER CONSUMABLES STATUS AS OF 8-11-99/8-13-99

| Spacecraft | Consumption One Week (Gm) | Propellant Remaining (Kg) | Output (Watts) | Margin (Watts) |
| --- | --- | --- | --- | --- |
| 31 | 6.32 | 32.26 | 321.3 | 40 |
| 32 | 13.31 | 34.05 | 322.9 | 68 |

RANGE, VELOCITY AND ROUND TRIP LIGHT TIME AS OF 8/20/99

|  | Voyager 1 | Voyager 2 |
| --- | --- | --- |
| Distance from the Sun (Km) | 11,196,000,000 | 8,776,000,000 |
| Distance from the Sun (Mi) | 6,957,000,000 | 5,453,000,000 |
| Distance from the Earth (Km) | 11,167,000,000 | 8,672,000,000 |
| Distance from the Earth (Mi) | 6,939,000,000 | 5,388,000,000 |
| Total Distance Traveled Since Launch (Km) | 13,000,000,000 | 12,234,000,000 |
| Total Distance Traveled Since Launch (Mi) | 8,078,000,000 | 7,602,000,000 |
| Velocity Relative to Sun (Km/sec) | 17.294 | 15.829 |
| Velocity Relative to Sun (Mi/hr) | 38,684 | 35,408 |
| Velocity Relative to Earth (Km/sec) | 43.880 | 38.292 |
| Velocity Relative to Earth (Mi/hr) | 98,157 | 85,655 |
| Round Trip Light Time (Hours:Minutes:Seconds) | 20:41:46 | 16:04:18 |